## Slide 1: Cloud: parcel? Model?
By Chenxi Qiu & Edward Groot

## Slide 2: Content
The content

## Slide 3
θ
Melting
Condensation
Evaporation
Freezing (&ice deposition)
Mixing
W
Buoyancy*
Cloud content
Mass
Mixing
Mixing
Model: dynamic equations – sources/sinks

## Slide 4
VAPOR
M
0°C
F
-38 °C
D
First step
Second step
Third step
WL > WL.thres
WI > WI.thres
C
100% RH
Parameterization based on Rotstayn et al. (2000), between 0 and -38°C
Slow
Fast
E
<100% RH
Model: moisture & cloud processes
Leaves parcel

## Slide 5: Dynamic entrainment
Environmental air is trapped by the convective cloud; (vertical) length scale of this process depends on the parcel size
; “equivalent radius”, assuming CP is spherical
Conservation (of water) check if μ set to 0
Many other parameters are also set to a reference value, e.g. initial and then varied

## Slide 6: Environmental profile + assumptions
Observations of August 26th 2010 12 UTC/GMT in Essen, Germany
Slightly modified, assuming enriched moisture at ±3 km
Classical “surface based” convection
Linear interpolations between nearest levels
Initial small disturbance T & water vapor
Convective rain event in Gelderland & Overijssel

## Slide 7: No entrainment
Mean precipitation over the final area of the parcel: 4.40 mm
time
isotherms
Z (m)
0 °C
time

## Slide 8: Constant entrainment
Cinvr = 0.00, Mean precipitation over the final area of the parcel: 3.97 mm
isotherms
Z (m)
0 °C
time
time

## Slide 9: Full entrainment
Reference run - = 5e-5 & = 0.16: 4.99 mm areal mean precipitation
isotherms
Z (m)
0 °C
time
time

## Slide 10: Very sensitive
Both momentum eq.
And phase of cloud content
Minor changes
(including time step)
lead to very different results
Tmelt

## Slide 11: Change of μ0 to 0
Mean areal precipitation of 4.40 mm

## Slide 12: Change of μ0 to 2e-5
Mean areal precipitation of 4.29 mm
We did more experiments

## Slide 13: Change initial Req
Reference value: 2500 m; reasonable values 300-5000 m
No cloud at 10 m and negligible at 100 m
At 500 m: cloud with negligble ice content, very little precipitation (<0.1 mm)
But cloud has relevance for environmental moisture at z = 2.5-3 km
With 2500 m: result already shown as “full entrainment”

## Slide 14: Change initial Req: 5000 m
Mean areal precipitation is 9.22 mm.

## Slide 15: Sensitivity cloud water to ice conversion
If we set the ice initiation lower, little ice is initiated and less (mostly “warm”) precipitation can be produced
At superfast rate (mean precipitation 3.7 mm): 100% ice at 260 K
Heat of fusion may be important buoyancy push, although small (< 2K)
Cconv=50 Cconv=1

## Slide 16: Sensitivity upper air moisture
Reduction of moisture above 2 km
Reduction | Precipitation
5% | 2.34
25% | 0.34
50% | 0.18
99% | 0.11

## Slide 17: Discussion
Horizontal dynamics excluded in parcel model, but essential as “sorting mechanism”

## Slide 18: Discussion
No oscillatory behavior in reality, but either dissipation or persistance due to role of horizontal dynamics
In this model, condensed water or ice is either inside or outside the parcel but does not go somewhere
Interaction parcel & cloud content
Limitation of parcel model
Over-sensitivity of mixed clouds for 260-273 K temperature?
But in general the parameterizations (foremost conversion to ice) are hugely simplified
No sublimation/riming (via liquid water)

## Slide 19: Conclusion

## Slide 20: Thank you for your attention